## Slide 1: Fundamentals of Networking
NETWORKING
AND IP ADDRESSING
PREPARED BY:
AMINU IDRIS
(CCNA, CompTIA Security+, CEH, OSCP, CISSP, CISM )

## Slide 2: Addressing Schemes
FLAT
Used by Intranetworks
Used by Layer 2
Used in MAC address
Is assigned statically based on next available number or random
  Social Security Number
  Your Name
  MAC- C0:AD:00:23:4F:89
HIERARCHICAL
Used by Internetworks
Used by Layer 3
Used by IP address
Is assigned dynamically based on your location
  Phone System
  ZIP Code
  IP- 182.157.63.219

## Slide 3: Internet Protocol Address (IPAddress)
A unique numerical label assigned to each device participating in a network
Every device on the Internet must have a unique IP address to identify itself
Internet Assigned Numbers Authority (IANA)
Manages the IP address space allocations globally
Delegates five regional Internet registries (RIRs) to allocate IP address blocks to local Internet registries (Internet service providers)
For an IP to be routable over the Internet, it must have:
  IP address
  Subnet Mask
  Default Gateway
  DNS address (only for address lookup, i.e. web sites)

## Slide 4: Types of Addressing
Static IP address
  Manually assigned to a device by an administrator
  Constant and does not change.
Dynamic IP address
  Assigned to device each time it starts
  Requires less human intervention
  Less administration
  Uses Dynamic Host Configuration Protocol (DHCP)
  Enabled by default
  No user intervention

## Slide 5: Classful vs Classless
CLASSFUL
Divided into 5 classes A, B, C, D
(multicast) and E (reserved)
Does not send subnet information
All networks are the same size
Have the same subnet mask
CLASSLESS
Also known as CIDR (Classless Inter-Domain Routing)
Sends subnet information
Network can be different sizes
Networks can have different
subnet masks using VLSM (Variable Length Subnet Mask)
5

## Slide 6: Network& Host Number Formulas
The formulas are the default configuration for each class:
1.N = Network Number
Assigned by the American Registry for Internet Numbers (ARIN)
Administrator has no control over this part of the address
2.H = Host Number
Assigned and controlled by the network administrator
 | 1 Byte 8 Bits | 1 Byte 8 Bits | 1 Byte 8 Bits | 1 Byte 8 Bits
Class A | N | H | H | H
Class B | N | N | H | H
Class C | N | N | N | H

## Slide 7: Class A Addresses
First octet only identifies the network
When written in a binary format, the first (leftmost) bit of a Class A address is always
0 (zero)
Class A IP address example: 124.95.44.15
Range from 1-126 in their first octet
127 is part of a class A range but has been reserved for loopback testing
Zero (0) can’t be used
Remaining three octets can be used for the host portion of the address
224 or 16,777,216, possible IP addresses per class A network
Class A |  |  | 
8 Bits | 24 Bits |  | 
Network | Host | Host | Host

## Slide 8: Class B Addresses
When written in a binary format, the first (leftmost) bit of a Class B address is always 10 (one and zero)
Class B IP address example: 151.10.13.28
The first two octets identify the network number assigned by ARIN
Range from 128 to 191 in their first octet
Remaining two octets can be used for the host portion of the address
216 or 65,536, possible IP addresses per class B network
Class B |  |  | 
16 Bits |  | 16 Bits | 
Network | Network | Host | Host

## Slide 9: Class C Addresses
When written in a binary format, the first (leftmost) bit of a Class C address is always 110 (one, one and zero)
Class C IP address example: 201.110.213.28
The first three octets identify the network number assigned by ARIN
Range from 192 to 223 in their first octet
Last octet can be used for the host portion of the address
28 or 256, possible IP addresses per class C network
Class C |  |  | 
24 Bits |  |  | 8 Bits
Network | Network | Network | Host

## Slide 10: Address Ranges
IMPORTANT!!!
MEMORIZE
N.H.H.H
N.N.H.H
N.N.N.H
1 – 126
128 – 191
192 – 223
Class A Class B Class C

## Slide 11: NetworkAddress
Ends with binary 0s in all host bits
Also know as the wire address
Never used as a device IP address
Used by routers to forward data
Example IP address: 152.21.2.3
  Class B
  First two octets are assigned
  Last two octets are host numbers used for devices in the network
  Network address: 152.21.0.0
Network |  |  |  | Host |  |  | 
32 Bits |  |  |  |  |  |  | 
152 | . | 21 | . |  | 0 | . | 0

## Slide 12: Examples of Network Numbers
2. 117.23.8.3
3. 156.132.64.12
4. 208.150.112.16
5. 91.118.125.2
What is the network number for this IP address?
1. 194.78.112.6 194.78.112.0
117.0.0.0
156.132.0.0
208.150.112.0
91.0.0.0

## Slide 13: Broadcast Address
End with binary 1s in host bits
Used to send data to all devices on a network
Never used as a device IP address
Example IP address: 152.21.2.3
  Class B address
  First two octets are assigned
  Last two octets are host numbers used for devices in the network
  Broadcast address: 152.21.255.255
Network |  |  |  | Host |  |  | 
32 Bits |  |  |  |  |  |  | 
152 | . | 21 | . |  | 255 | . | 255

## Slide 14: Examples of Broadcast Address
What is the Broadcast address for this IPaddress?
1. 194.78.112.6
2. 117.23.8.3
3. 156.132.64.12
4. 208.150.112.16
5. 91.118.125.2
194.78.112.255
117.255.255.255
156.132.255.255
208.150.112.255
91.255.255.255

## Slide 15: Network Numberand Broadcast Address
All 0’s in the host address is the Network Number
All 1’s in the host address in the Broadcast Address
These two addresses can never be used when assigning IP’s
When finding the number of useable host addresses, you will always subtract 2 (network & Broadcast)

## Slide 16: Default Subnet Mask
Formal name: Extended Network Prefix
Tells the network devices which part of an address is the network field and which part is the host field
32 bits long and 4 octets, just like an IP address
Step to determine the subnet mask:
  Express the subnetwork IP address in binary form
  Replace the network portion of the address with all 1s
  Replace the host portion of the address with all 0s
  Convert the binary expression back to dotted-decimal notation

## Slide 17: Examples of Default Subnet Mask
What is the Default Subnet Mask for this IPaddress?
1. 194.78.112.6
2. 117.23.8.3
3. 156.132.64.12
4. 208.150.112.16
5. 91.118.125.2
255.255.255.0
255.0.0.0
255.255.0.0
255.255.255.0
255.0.0.0

## Slide 18: Default Subnet Mask
Class | Formula | Slash Notation | Default Mask
Class A | N.H.H.H | /8 | 255.0.0.0
Class B | N.N.H.H | /16 | 255.255.0.0
Class C | N.N.N.H | /24 | 255.255.255.0

## Slide 19: Default Gateway
A port on a router
Your connection to the Internet
IP address MUST be part of the network
Usually the first or last IP address in the network